## Slide 1
Piezo Pickup Processor the Pickgaurd
Ghost Piezo Electric Saddles
PCB with Kinetis MCU

## Slide 2
Piezo Pickup Processor – Design Constraint
Each Pickup is individually sampled. One Sampling Channel for each string.
FPGA must Digitally sum the 6 channels, Apply filter + volume control, send results to DAC through standard JACK.
S/PDIF output.
FPGA Filter is remotely programmable by external microcontroller
External Microcontroller has ADCs to sample 2, control potentiometers and switches
External Microcontroller can store FPGA configuration
Microcontroller has USB interface to upload new configuration and parameters.
CAT 5 cable jack to receive power and to send digital audio and balanced line analog.
High-Speed USB to send all 6 pickup outputs to PC.

## Slide 3
Freescale Kinetis K20
Piezo (E)
Piezo (B)
Piezo (G)
Piezo (D)
Piezo (A)
Piezo (E)
Signal Conditioning
Signal Conditioning
Signal Conditioning
Signal Conditioning
Signal Conditioning
Signal Conditioning
Signal Conditioning
6x ADC Inputs
I2S Bus
Control
Wheel
Control
Slider
Control Buttons
SPDIF Transmitter
JTAG Interface (OSBDM)
Balanced Line Driver
CAT 6e Jack
¼” Jack
USB Mini-B
System Power
USB Interface
DAC Out